## Slide 1: FOSDEM Network
What is DNS64 and NAT64; and why should you care?

## Slide 2: Who are we ?
Richard Hartmann – Network and project manager at Globalways AG
Peter Van Eynde – Cisco TAC – solving problems for a living
Andrew Yourtchenko – IPv6 Transition Engineer @cisco

## Slide 3: WHY OH WHY ?

## Slide 4: IPv4 has run out.

## Slide 5: Also at FOSDEM !
Pool Wifi-client-dualstack :
Utilization mark (high/low) : 100 / 0
Subnet size (first/next) : 0 / 0
Total addresses : 4094
Leased addresses : 4093
Excluded addresses : 0
Pending event : none
1 subnet is currently in the pool :
Current index IP address range Leased/Excluded/Total
0.0.0.0 151.216.48.1 - 151.216.63.254 4093 / 0 / 4094

## Slide 6: Also at FOSDEM !
Pool Wifi-client-dualstack :
Utilization mark (high/low) : 100 / 0
Subnet size (first/next) : 0 / 0
Total addresses : 4094
Leased addresses : 4093
Excluded addresses : 0
Pending event : none
1 subnet is currently in the pool :
Current index IP address range Leased/Excluded/Total
0.0.0.0 151.216.48.1 - 151.216.63.254 4093 / 0 / 4094
Pool Wifi-client-FOSDEM14 :
Utilization mark (high/low) : 100 / 0
Subnet size (first/next) : 0 / 0
Total addresses : 8190
Leased addresses : 853
Excluded addresses : 0
Pending event : none
1 subnet is currently in the pool :
Current index IP address range Leased/Excluded/Total
151.216.3.151 151.216.0.1 - 151.216.31.254 853 / 0 / 8190

## Slide 7: Why not IPv5 ?
Internet Experiment Note IEN-119[1] (1979)
Never made it to public use
The version numbers are allocated only once

## Slide 8: IPv6
64 bits in an address should be enough ?
We need variable length addresses !
  (unlimited !)
No, it has to be fixed length
256 bits -> 2^256 = 1.15 * 10^77
  Number of atoms in the universe: ~10^80
  Too much !
  Compromise: 128 bits

## Slide 9: Problem
&

## Slide 10: Mexican standoff
Clients
Content
Carriers
Applications
Hardware

## Slide 11: World IPv6 day
Lets turn it on and see what breaks

## Slide 12: World IPv6 launch
http://www.worldipv6launch.org/

## Slide 13: Today’s production dualstack content
Google
Facebook
Yahoo
Youtube
Netflix
Akamai
Many many others

## Slide 14: Where are the users ?
http://en.wikipedia.org/wiki/File:Oftheunicorn.jpg

## Slide 15: Country #1

## Slide 16: Country #2

## Slide 17: Country #3

## Slide 18: Country #4

## Slide 19: Country #5

## Slide 20: Conclusion: unicorns definitely exist.

## Slide 21: BUT THIS NOT ENOUGH !

## Slide 22: IP at FOSDEM

## Slide 24
You are here

## Slide 25: Time for the next step
Dualstack is working
  As long as you have IPv4 addresses to spare
  You don’t have them (Remember ‘why IPv6’?)
Need to run NAT anyway
One address space to manage
  cheaper
  Easier
  faster
 Let’s switch off IPv4

## Slide 26: But what about legacy Internet ?
http://www.internetsociety.org/deploy360/blog/2013/07/the-legacy-ip-only-ipv6-horse-and-buggy-stickers-how-to-get-copies/

## Slide 27: IPv6 space is big.

## Slide 28: IPv6 space is big.
VERY BIG

## Slide 29: How big ?
IPv6 space is denoted in blue
IPv4 space is denoted in red

## Slide 30: Let’s zoom in: blue is a single /64 subnet
Home users typically get at 256 of these (/56)

## Slide 31: We can hide a complete Legacy Internet in a /96 !
But how ?
Try to connect to http://guardian.co.uk/
  DNS request AAAA & A records
  Response with A only
  Now what ?

## Slide 32: We can hide a complete Legacy Internet in a /96 !
But how ?
Try to connect to http://guardian.co.uk/
  DNS request AAAA & A records
  Response with A only
  Now what ?
YOU LIE !

## Slide 33: DNS64
Pick an IPv6 prefix (there’s enough space!)
Map IPv4 into that space
Tell your DNS server to synthesize AAAA from the A records if no AAAAs are returned

## Slide 34: DNS64
IPv6 prefix
2001:db8::/64
IPv4
0.0.0.0/0
IPv6-mapped
2001:db8::/96

## Slide 35: DNS64 configuration on the BIND
/etc/bind/named.conf.options:
dns64 2001:db8::/96 {
clients { any; };
}

## Slide 36: DNS64
IPv6 Internet
IPv4-only server
IPv4
192.0.2.1
IPv6
IPv6-only Site
IPv6 interface
IPv4 interface
DNS64
DNS
www.legacywebsite.example ?
www.legacywebsite.example ?
A: 192.0.2.1
A: 192.0.2.1
AAAA: 2001:db8::c000:0201
-w -pedantic: Several simplifications were made while creating this slide.

## Slide 37: NAT64
IPv6 Internet
IPv4-only server
IPv4
72.163.4.161
IPv6
IPv6-only Site
IPv6 interface
1
s: [2607:f128:42:73::2]:37897
d: [2001:db8::192.0.2.1]:80
IPv4 interface
3
s: 153.17.16.82:1056
d: 192.0.2.1:80
2
asr1knat64#sh nat64 trans
tcp 192.0.2.1:80 [2610:d0:1208:cafe::c000:201]:80
153.16.17.82:1056 [2607:f128:42:73::2]:37897
4
s: 192.0.2.1:80
d: 153.17.16.82:1056
5
s: [2001:db8:72.163.4.161]:80
d: [2607:f128:42:73::2]:37897

## Slide 38: RESULTS

## Slide 46
Clearly, this is not good enough.

## Slide 47
FOSDEM’14 is the first general-purpose conference
With IPv6-only as a default
You all are part of history

## Slide 48
Do we continue
tomorrow ?